## Slide 1: The Gamma-ray Transients Monitor (GTM) on board Formosat-8B
Chih-hsun LIN
Institute of Physics, Academia Sinica, TAIWAN
On behalf of the GTM team
2nd Bilateral Meeting of Czech-Taiwan Collaboration in Astronomy

## Slide 2: Outline
FS8 mission and science goal
Instrument design and tests
Isotopes calibration
Summary

## Slide 3: Project Organization
Prof. HK Chang / NTHU
Project Investigator
Science goals
Detector simulation
Science data center
Data analysis and archive
Miss Christine Tan
Project Manager
Project management
Procurement
Documentation
Prof. CC Tsao/ NTHU
Co-PI
Mechanical design
Thermal design
Structure and thermal analyses
Dr. CH Lin/ NTHU
Co-PI
System design
Electronics design
Environmental tests
Taiwan Space Agency
Funding Agency
FS8B Satellite

## Slide 4: Formosat-8 Mission
FORMOSAT-8, remote sensing satellite program with 6 satellites in serial, is a priority mission of the 3rd phase of Taiwan space program.
Common platform for all of the satellite missions in the 3rd phase space program.
Test platform for science and advanced payloads.
Size : 120 cm x 140 cm x 160 cm Weight : 400 kg Orbit : 561 km, sun-synchronous orbit

## Slide 5: Science goal of GTM on board Formosat-8B
Monitor Gamma Ray Bursts (GRBs) and bright gamma-ray transients from other sources in 30 keV – 1 MeV.
Measurements of directions, counting rates and energy spectrums.
Whole sky coverage.

## Slide 6: Sensor module design
Based on GAGG scintillating crystals arrays and Hamamatsu SiPM arrays.
One sensor module:
  Size : ~ 50 mm x 50 mm x 8 mm
  Weight : ~ 146 g
  4 crystal blocks with 16 readout channels in total.
Total 64 channels for 4 sensor modules of a GTM unit.
1
2
3
4

## Slide 7: Expected Detection Performance
Use Fermi/GBM 10-year GRB fluence distribution (von Kienlin et al., 2020)
Consider a 36% duty cycle per orbit
FS8B/GTM will detect about 50 GRBs per year.
LGRB
SGRB
50% efficiency

## Slide 8: Detector response (50-300 keV) of the 8 sensors in different directions in the sky
Be linearly enlarged from 1,600 to 41,168 lattices.

## Slide 9: Localization Capability (Two LGRB cases)
4x10-6 erg/cm2
4x10-5 erg/cm2

## Slide 10: Mechanical and thermal designs
Weight budget: 1 kg/unit
  Four sensor modules ~ 600 g
Frame structure with multiple parts
  Light weight and easy manufacturing
  Easy to revise and replace
  Truss structure with high rigidity in limited mass.
Sufficient heat conduction verified by analysis and tests.

## Slide 11: Readout module design
Two 32 channel CITIROC FE ASICs
  Input charge to analog voltage output.
  Self-trigger with adjustable trigger threshold
  Two multiplexed analog outputs (HG and LG = 0.1 HG)
  Adjustable gains (1 to 600)
IGLOO2 FPGA for control and communications
  Telemetry/Commands: RS422 UART, 115200 bps.
  Data: SpaceWire 10M bps = 1M Byte/sec.
Maximum trigger rate ~ 44.9 kHz
No active thermal control.

## Slide 12: GTM Flight Model Assembly

## Slide 13: GTM Flight Model Assembly

## Slide 14: GTM FM Environmental Tests – FS-8 COTS Test Flow
EQM
FM

## Slide 15: Vibration Tests

## Slide 16: Thermal Vacuum Test

## Slide 17: Thermal Vacuum Test
-5oC
0oC
+5oC
+10oC

## Slide 18: SiPM Gain vs Temperature
Gain  -T
Dedicated calibration for each channel.
Good linear fitting with slope ~ -0.4 per oC (LG/HG=2/20)

## Slide 19: GTM is ready for flight.

## Slide 20: Isotopes Calibrations
Isotopes/Material | Gammy Ray (keV) | XRF (keV) | Gain (LG/HG)
BaSO4 |  | 35 (Ba) | 2/20
133Ba | 81 &356 |  | 2/20
57Co | 122 |  | 2/20
LYSO | 88, 202 & 307 | 55 (176Lu) | Both
22Na | 511 & 1274 |  | 1/20
137Cs | 662 |  | Both
60Co | 1173 & 1332 |  | 1/20

## Slide 21: LYSO Calibration (LH/HG=2/20)
20oC
-10oC
Unexpected Bumps close to the analog output limit of FE ASIC.
Cut

## Slide 22: Cross-talk noise study
Many events with more two pixels fired.
  Compton events
  Light sharing
  Cross-talk noises
Plot energy ratio of minor pixels (neighboring pixels) and major pixel.
Center Case
Edge Case

## Slide 23: Cross-talk noise study
Cut
20oC
-10oC

## Slide 24: Linear Energy Calibration with LYSO (LH/HG=2/20)
307
202
88
55 (Lu)
509
(202+307)
35 (Ba)
Use 55 keV, 202 keV and 307 keV for linear fitting.
Good linear relation between gamma-ray energy and measured ADC value up to ~500 keV.
Plan to use 35 keV for in-flight calibration.

## Slide 25: SiPM Saturation Effect
56,000 *74% * 40% = 16,576 > 14,336 ⇒ Saturation occur!
(SiPM pixels#)
(Light#/MeV)
(Kotera et al., 2015)
662 keV
511 keV
307 keV
202 keV
122 keV
81 keV
1274 keV
662 keV
202 keV
307 keV
(Detection efficiency)
(Fill factor)

## Slide 26: Isotopes Spectrums
*room temperature (~25oC)

## Slide 27: Energy Resolution
Energy (keV) | Resolution (%) (FWHM/Peak)
81 | 26.4
122 | 24.3
202 | 25.4
307 | 20.2
356 | 20.4
511 | 17.9
662 | 16.5
1173 | 19.1
1274 | 17.6
1332 | 18.0
(PMT)

## Slide 28: Summary
GTM is ready for flight. The integration with the FS8B bus is scheduled in 2025, Q1.
The detail calibration for gamma-ray energies measurements has been performed. GTM can measure gamma rays with energies up to 1 MeV at least.
This information will be used to optimize settings for flight.