## Slide 1: Paper Study
A two-stage time-stretching TDC with discrete components
2505.07514

## Slide 2: The idea
time-stretching
But dead time also get stretching
S (stretched factor) = I2 / I1
Dead time
Charge rate
Discharge rate
M2 (PMOS) turn on when no signal input
vth

## Slide 3: The idea
two-stage time-stretching
To solve dead time problem
Assume clk = 100MHz, T = 10ns, S0 = S1 = S2 = 10

## Slide 4: Prototype

## Slide 5: On board pulse generator
ns-level pulse generator
Press SW1 to generate pulse
modify R1 to change oulse width

## Slide 6: one-stage
non-linear
as calibration lookup table

## Slide 7: one-stage
20ns input: 60.1 ps RMS jitter
10ns input: 47 ps

## Slide 8: two stage
edge detection (seem to perform by FPGA)
second stage stretching

## Slide 9: two-stage
non-linear

## Slide 10: two-stage
20ns input
edge 1: 75.5 ps RMS jitter. edge 2: 67.8 ps RMS jitter

## Slide 11: edge detection

## Slide 12: two stage
less than 120 ps per unit ( < 170ps combined)
less than 17ps after S0 division

## Slide 13: total time resolution
Counter quantization error, 41ps
Figure 7
Figure 11
Figure 12

## Slide 14: result
The prototype TDC’s overall time resolution was measured by comparing direct oscilloscope
The discrete-component prototype demonstrates that two-stage time-stretching TDCs can achieve 60–100 ps resolution using only a 100 MHz clock counter.

## Slide 15: summary
The design and test results of a two-stage time-stretching prototype TDC made with low-cost discrete components
A less than 100 ps time resolution is achieved with a 100 MHz clock counter.
The time resolution of such a TDC is found to be dominated by the time jitter of the first-stage stretching unit. The conversion time for a 10 ns input width is less than 300 ns, a factor of five less than a single stage stretching with a stretching factor of 100.
A stepping stone and optimization platform towards the design of TDC in modern CMOS technologies for future 4D pixel detectors at hadron colliders, which requires 𝜇W level power consumption, < 50 ps level time resolution, and with more than 100 kHz hit rate.
The prototype is also a ready-to-use low-cost system for many existing applications where a 100 ps level resolution is enough, such as precision timing circuits for neutrino detectors.

## Slide 16: Thank you for listening
Q / A