## Slide 1: Weekly Meeting 20251109
Chia-Yu Hsieh
Academia Sinica, Taiwan

## Slide 2: Task List
RPC
  Test carbonless RPC
  Test discriminator : shaper & delay line unction
  Discriminator production => quotation
  Discriminator control => 佩蓉
DY analysis
  Test COMPASS data => postponed to Jan.
ZDC
  MC : Official MC simulation with ECAl = ZDC crystal or Wsi => today
  Hardware : deal with noise, prepare online monitoring, H2GCROC operation => work w/ students
MCFM + xFitter
  - DYNNLO test

## Slide 3: WSi Branch
epic_zdc_lyso_sipm.xml : <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_Crystal_LYSO.xml"/>
epic_zdc_wsi_hg1_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_1.xml"/> epic_zdc_wsi_hg2_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_2.xml"/> epic_zdc_wsi_hg3_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_3.xml"/> epic_zdc_wsi_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_LG.xml"/>
https://github.com/alillari/epic-UConn-ZDC-WSi
Not sure what is the difference between them now.
I now choose to run “epic_zdc_lyso_sipm.xml” and “epic_zdc_wsi_sipm.xml” to first make sure the framework work. Plan to run 100MeV-40GeV gamma and 1GeV to 300GeV neutron. Then check energy resolution and position resolution.
I will study the other configurations later.

## Slide 4: epic_zdc_lyso_sipm.xml
/usrX/cyhsieh/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/epic_zdc_lyso_sipm.xml:
<include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_Crystal_LYSO.xml"/>
Active area = 60cm*60cm
Position
  ionCrossingAngle = ICA = -0.025 rad
  (x, y, z) = (r*sin(ICA), r*cos(ICA), 35.8564 m)
  (defined in ~/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/compact/definitions.xml
LYSO crystal = 3cm*3cm = 20 crystals

## Slide 5: epic_zdc_wsi_sipm.xml (20 pad layer, No pix layer)
/usrX/cyhsieh/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/epic_zdc_wsi_sipm.xml:
<include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_LG.xml"/>
Xml file = <define> + <detector> + <readout>
WSi layer
  20 layers “PAD” Wsi (no Pixel layer)
  1 layer = W (3.5mm) + glue (0.11um, G10) + Si pad (320mm, Si) + glue (0.11um, G10) + PCB (1.6mm, PET) + Air (1mm)
  Si pad = 1cm*1cm => 60 pads / layer
structure
<detector>

## Slide 6
position
Material thickness
Pad info
<readout>
<define>

## Slide 7: epic_zdc_wsi_hg1_sipm.xml 17 pad + 3 pixel (3, 6, 9)
/usrX/cyhsieh/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/epic_zdc_wsi_hg1_sipm.xml:
<include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_1.xml"/>
Xml file = <define> + <detector> + <readout>
WSi layer
  20 layer = 17 layers “PAD” Si + 3 layer “Pixel” Si
  1 layer = W (3.5mm) + glue (0.11um, G10) + Si pad/pixel (320mm/300mm, Si) + glue (0.11um, G10) + PCB (1.6mm, PET) + Air (1mm)
  Si pad : 1cm*1cm, 60cm*60cm/1cm*1cm = 60 pads / layer
  Si pixel : 0.5mm* 0.5mm, 1,440,000 pixel / layer

## Slide 8
1, 2
3
{10..20}
+
4, 5 (pad) + 6 (pixel)
7, 8 (pad) + 9 (pixel)
+

## Slide 9: epic_zdc_wsi_hg2_sipm.xml 17 pad + 3 pixel (4, 8, 12)
/usrX/cyhsieh/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/epic_zdc_wsi_hg2_sipm.xml:
<include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_2.xml"/>

## Slide 10: epic_zdc_wsi_hg3_sipm.xml 17 pad + 3 pixel (5, 10, 15)
/usrX/cyhsieh/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/epic_zdc_wsi_hg3_sipm.xml:
<include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_3.xml"/>

## Slide 11: Position Resolution Study

## Slide 12: Alessio’s Work
2D hit map, 2D position map, layer by layer

## Slide 13: Alessio’s Work
Get position in x and y layer by layer
Linear fit to get track
Compare w/ mc particle
Position resolution layer by layer?
(but no hit info in mc particle? How to compare?)

## Slide 14: Alessio’s Work

## Slide 15: epic_zdc_lyso_sipm.xml
/usrX/cyhsieh/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/epic_zdc_lyso_sipm.xml:
<include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_Crystal_LYSO.xml"/>
Active area = 60cm*60cm
Position
  ionCrossingAngle = ICA = -0.025 rad
  (x, y, z) = (r*sin(ICA), r*cos(ICA), 35.8564 m)
  (defined in ~/2024ZDC/eic/epic-UConn-ZDC-WSi/install/share/epic/compact/definitions.xml
LYSO crystal = 3cm*3cm = 20 crystals

## Slide 16: ECAL : epic_zdc_lyso_sipm, 40GeV, gamma
20 pos in x => ok
20 pos in y => ok
20 pos in z => ? => ok (detector rotates with y axis)
I will try to change xml file and move detector perpendicular to z axis. So that we will have one z position and better to work on position resolution study.

## Slide 17: HCAL Structure
Material and thickness of one layer
64 layers

## Slide 18: HCAL : sipm on tile, 40GeV, gamma
X, Y binning is not very important

## Slide 19: HCAL : 64 layer in Z
Find Z binning to define layer
One layer, one defined hit position
Find tracking based on hits from each layer
Also , check profile layer by layer

## Slide 20: Put Detector Straight!
All checked by display!
Center at (0, 0, z)
LYSO z =3570, 3577 (ecal) , 3580, 3741 (hcal)
WSi z = 3579, 3592 (ecal) , 3593, 3754 (hcal)
s

## Slide 21: Put Beam along Zaxis (steering.py)

## Slide 22: ECAL

## Slide 23: HCAL

## Slide 24: Beam Profile layer by layer
ECAL => reserve layer#0-layer100 (1-20 layer)
HCAL => reserve layer#1-layer#64 (64 layer)
One raw hits
One weighted method
=> check evt by evt first
=> check “lyso crystal” + “sipm on tile”

## Slide 25: ECAL : Hits in XY
Raw hits (color weighted by Edmp)
LYSO crystal : only one layer

## Slide 26: ECAL : Hits in XZ and YZ
Raw hits (color weighted by Edmp)
Energy-weighted hit position

## Slide 27: HCAL : Hits in XY
Raw hits (color weighted by Edmp)
sipm-on-tile : 64 layers

## Slide 28: HCAL : Hits in XZ and YZ (fit pol0)
Raw hits (color weighted by Edmp)
Energy-weighted hit position

## Slide 29: Apply cut on Multiplicity?
nHit<50, exclude the layer?

## Slide 30: HCAL : Hits in XZ and YZ(fit pol1)
Raw hits (color weighted by Edmp)
Energy-weighted hit position

## Slide 31: HCAL : Hits in XZ and YZ (fit pol1, nhit/layer>5)

## Slide 32: HCAL : Hits in XZ and YZ (fit pol1, nhit/layer>5)

## Slide 33: Residual @ 64 layers (64 Residual for one event)
X

## Slide 34: y

## Slide 35: Residual @ Weighted-Z position (One Residual for one event)