## Slide 1: EIC-ASIA ZDC ECAL Test Beam Analysis
Wen-Chen Chang, Kai-Yu Cheng, Tatsuya Chujo, Yuji Goto, Chia-Yu Hsieh, Motoi Inaba, Subaru Ito, Kentaro Kawade, Yongsun Kim, ChiaMing Kuo, Chih-Hsun Lin, Po-Ju Lin, Rong-Shyang Lu, Jen-Chieh Peng

## Slide 2: (Review) 2nd ZDC ECAL Prototype
Readout boards
Moving stage (remote control) ~ 54cm
Beam
PbWO4 + SiPM
LYSO + APD
~27cm
Beam monitor : Trigger system
 | Detector | Crystal |  |  |  | Sensor |  | DAQ
 |  | name | Size of one cell | Length | Array | Type | sensor/crystal | 
2nd prototype 2024-2025 | LYSO + APD | LYSO | 1cm*1cm | 6.6cm (6X0) | 8x8 | APD C30739ECERH | 1 | CITIROC
 | PbWO4 + SiPM | PbWO4 | 2cm*2cm | 5.3cm (6X0) | 6x6 | SiPM Onsemi MICROFC-60035 | 2 | CITIROC

## Slide 3: (Review) 2nd ZDC ECAL Prototype
Preliminary results gave energy resolution without energy regression.
LYSO + APD = 36.91%
( > 15% requirement)
PbWO4 + SiPM = 14.95%
( > 15% requirement)
LYSO + APD ~ 35%
MC : 10-40GeV gamma
PbWO4 + SiPM ~ 15%
706 MeV e+

## Slide 4: To Improve the results
Study beam angle cut
Study residual cut
Study energy spread
Study threshold cut
Energy regression

## Slide 5: Study Beam Angle Cut (1) Beam Track Reconstruction
Both monitors contain x and y readout planes to measure the horizontal and vertical beam positions, respectively. The beam position was determined from the energy-weighted average of the hit coordinates (8x8 arrary), where the ADC value of each channel (is used as the weight) :
MC
Datat
MC
Data
Mean
BM is around 10cm away from ZDC
Theta is defined as the angle between red and blue line.
Data has larger angle compared to MC.

## Slide 6: Study Beam Angle Cut (2) : MC Setting
Objective: Energy deposition in the crystal array
Particle: Positron (PDG ID = −21)
Beam energy: W-200 μm–30
Beam position: ZDC center
Beam direction: perpendicular to ZDC surface (pencil beam)
Experimental Setup : same as test beam
No optical photon turned on
No APD/SiPM simulation

## Slide 7: Study Beam Angle Cut (2) : LYSO + APD
197 MeV, E5x5
(central ch)
197 MeV, E5x5 (Norm)
706 MeV, E5x5
706 MeV, E5x5 (Norm)
LYSO + APD :
No obvious improvement after beam angle cut

## Slide 8: Study Beam Angle Cut (3) : PbWO4 + SiPM
197 MeV, E5x5
(central ch)
197 MeV, E5x5 (Norm)
706 MeV, E5x5
706 MeV, E5x5 (Norm)
PbWO4 + SiPM :
No obvious improvement after beam angle cut
New
New

## Slide 9: Study Residual (1) : MC
The residual is defined as the difference between the predicted and true beam positions on the x and y axes:
where predicted position is from beam track extrapolation on ZDC and true position is center of center of crystal with maximum energy? The total residual represents the spatial deviation in two dimensions and is calculated as:
< 3.0 mm
@Z = ZDC face
< 1.4 mm
@Z = ZDC face
47 MeV
Norm- 47 MeV
Norm- 297 MeV
Norm- 396 MeV
Norm- 584 MeV
Norm- 796 MeV
2
1.4mm or 3 mm
(X,Y)true is center of main channel!!!

## Slide 10: Study Residual (2) : LYSO
Norm- 47 MeV
Norm- 297 MeV
Norm- 584 MeV
Norm- 796 MeV
2
No improvement applying extra radius cut?

## Slide 11: Study Residual (2) : PbWO4
Emax

## Slide 12: Study Residual (2) : PbWO4
Emax

## Slide 13: Study Energy Spread Cut (1) LYSO + APD
~50%
~25%
~60%
~10%
~10%
~10%
~10%
~10%
~10%
~10%
~5%
Emax
E5x5
No obvious improvement after energy spread study.

## Slide 14: Study Energy Spread Cut (2) PbWO4 +SiPM
先緩緩，計算方式會因為SIPM有兩頻道而產生很多問題，要再想想沒辦法立刻趕出來

## Slide 15: Pedestal Study (find ADC <=> Threshold (DAC))
LYSO crystal
GAGG
SiPM
CITI ROC
Set different threshold 220-620 (digit), experimental condition
Check energy spectrum
Then we can find threshold digit to energy relation plot
Fitting function:
  Gaussian: BG + 202keV + 307keV + 202 keV escape peak.
  Exponential: something background.
  Gaussian CDF: threshold cut.
  From the fitting, we can define threshold position
LYSO threshold range (digit, MeV)
PbWO4 threshold range (digit, MeV)
μTHR(DAC) = -3375 + 15.255 X + 0.017 X2 +2500
400DAC = 7947ADC , 650DAC = 16223ADC
MeV = (ADC+1367)/334
7947ADC = 10.88 MeV, 16223ADC = 31.84MeV
這邊要用單一SiPM頻道的校正去看，不能用ADC 11(會有兩SIPM)，所以你會看到校正因子不一樣，不是圖放錯
LYSO threshold range (digit, MeV)
=(main Ch.) 268~300 = ???~??? MeV
PbWO4 threshold range (digit, MeV)
=(main Ch.) 400~650 = 10.3~30.0 MeV)

## Slide 16: MC Setting
Objective: Energy deposition in the crystal array
Particle: Positron (PDG ID = −21)
Beam energy: W-200 μm–30
Beam position: spread beam
Beam direction: perpendicular to ZDC surface
Experimental Setup : same as test beam
With optical photon turned on
No APD/SiPM simulation

## Slide 17: LYSO/PbWO4
ADC <=> Energy mapping, Fitting method (1)
NO threshold cut, Data/MC : Emax, E3x3, E5x5 (3)
With threshold cut (exp), Data/MC : Emax, E3x3, E5x5 (3)
With threshold cut (match), Data/MC : Emax, E3x3, E5x5 (3)
Threshold VS Resolution : Data, MC (1)

## Slide 18: LYSO E-ADC mapping
1

## Slide 19: PWO E-ADC mapping
1
Data/MC
Data / Scaled-MC

## Slide 20: PbWO4: 1x1 Data/MC in different energy
(Data+3933)/(MCx397.47)
Data-3933
MCx397.41
Data FIT
MC FIT

## Slide 21: PbWO4: 3x3 Data/MC in different energy
Data-3933
MCx397.41
Data FIT
MC FIT
(Data+3933)/(MCx397.47)

## Slide 22: PbWO4: 5x5 Data/MC in different energy
Data-3646
MCx209.52
Data FIT
MC FIT
(Data+3933)/(MCx397.47)

## Slide 23: PbWO4: 1x1 Data/MC with THR
(Data+3933)/(MCx397.47)
Data-3933
MCx397.41
Data FIT
MC FIT

## Slide 24: PbWO4: 3x3 Data/MC with THR
Data-3933
MCx397.41
Data FIT
MC FIT
(Data+3933)/(MCx397.47)

## Slide 25: PbWO4: 5x5 Data/MC with THR
Data-3646
MCx209.52
Data FIT
MC FIT
(Data+3933)/(MCx397.47)

## Slide 26: PbWO4: 1x1 Data/MC with appreciate THR
(Data+3933)/(MCx397.47)
Data-3933
MCx397.41
Data FIT
MC FIT

## Slide 27: PbWO4: 3x3 Data/MC with appreciate THR
Data-3933
MCx397.41
Data FIT
MC FIT
(Data+3933)/(MCx397.47)

## Slide 28: PbWO4: 5x5 Data/MC with appreciate THR
Data-3646
MCx209.52
Data FIT
MC FIT
(Data+3933)/(MCx397.47)

## Slide 29: Threshold VS Resolution : Data, MC
1
Same graph in different art.
PbWO part was trying to apply the cut by the all setting which are used in Feb. 2025 beam test.
The magenta circle is the threshold for the analysis data, the magenta point is the “DATA”.
Do the comparison with data, the data is better then MC in THR = 30.0MeV case, and the closest case is THR = 25.7 MeV.

## Slide 30: Plan for the Test Beam next March
Original plan :
  PbWO4 + newSiPM + H2GCROC
New plan :
  PbWO4 + oldSiPM + CITIROC (full readout)
  PbWO4 + oldSiPM + H2GCROC
  LYSO + APD + CITIROC (full readout)
To do
Known problem for PbWO4 : threshold too high in last test beam (noisy)
CR test in Taiwan is undergoing to reduce noise
If we can fix the problem, we would like to test it again. PbWO4 + SiPM +CITIROC
Also to test w/ another DAQ, H2GCROC
Know problem for LYSO : Wrongly operation of APD

## Slide 31: CR Test