## Slide 1: ZDC Crystal Update 20251201
Chia-Yu Hsieh
Academia Sinica, Taiwan

## Slide 2: Yuji’s Request
BM and ZDC (Find ADC max)
  ADCx VS count
  ADCy VS count
  ADCx–ADCy
  BM w/o Calibration (peak) and ZDC w/ Calibration (weighted method)
Residual -> Position resolution
E5x5 -> Energy resolution

## Slide 3: Run Info
Feb2025, Run2013,

## Slide 4: Hit Distribution (RAW)
log
X-axis : change to cm?
Titile : BM1 X plane
X-axis : number of hit
Y-axis : log scale
Titile : BM1 X plane
ZDC
Same plot as BM
Separated into x and y in 1D

## Slide 5: Fired Position (Weighted Method, BM simple weight, ZDC gravity weight)
w/ Calibration
w/ tracking, timing and position matching are done.
Label => red.
Here, sigma is beam profile sigma

## Slide 6: Beam Profile w/ Different Method
Compare 3 method to determining the beam position in B.M.
1. ADC max in layers
  Take position of ADCmax channel X and Y.
2. ADC Wt. in layers
  Using gravity center method:
  wi = ADC of channel i
3. Unwt. in layers
  wi = 1 ( = Unwt. setting)
1st BM layers
2nd BM layers
1. ADC max in layers
3. Unwt. in layers
2. ADC Wt. in layers
 | ADC max | ADC Wt. | Unwt.
1st BM layers |  |  | 
 | 36.7 | 14.8 | 13.5
 | 113.4 | 25.5 | 18.7
2st BM layers |  |  | 
 | 125.1 | 41.68 | 21.36
 | 48.3 | 28.0 | 8.2
 | ADC max | ADC Wt. | Unwt.
1st BM layers |  |  | 
 | 36.7 | 14.8 | 13.5
 | 113.4 | 25.5 | 18.7
2st BM layers |  |  | 
 | 125.1 | 41.68 | 21.36
 | 48.3 | 28.0 | 8.2
Simple average => chosen for 2025 Feb. test beam

## Slide 7: Residual/Position Resolution
Residual: ZDC CM - B.M. CM prediction
Residual in R form
Residual: ZDC CM - B.M. ADCmax prediction
After tracking, time and position matching.
Resolution ~ X^2 = res_ZDC^2 + res_BM^2
Assuming resolution of BM = 2mm (too small compared to 6mm-8mm)
=> Resolution here is basically resolution of ZDC = 6mm~8mm
please fit and give sigma

## Slide 8: Clustering and Energy Resoltuion
Better plot => give Eax, E3x3, E5x5, separated.
X-axis change to energy (MeV)
E3x3
Emax
E5x5