## Slide 1: ZDC crystal part : online monitoring 20251205
Chia-Yu Hsieh On
Behalf on Taiwan ZDC crystal group

## Slide 2: Online Analysis Plot PbWO4 + oldSiPM + CITIROC
We develop online analysis display tool with a run took this year on Feb. (PbWO4+oldSiPM + CITIROC, run2013 with 796MeV positron beam)
The total estimated time needed to display the results : In total ~ 7mins to show the online analysis after data taking

## Slide 3: Raw Hit Distribution : BM1
Hits position : 2D
Hits position in X
Hits position in Y
Hit Multiplicity in X
Hit Multiplicity in Y

## Slide 4: Raw Hit Distribution : BM2
Hits position : 2D
Hits position in X
Hits position in Y
Hit Multiplicity in X
Hit Multiplicity in Y

## Slide 5: Raw Hit Distribution : PbWO4
Num of Hits : 2D
Num of Hits in X
Num of Hits in Y
Hit Multiplicity : 2D

## Slide 6: Raw Hit Distribution : PbWO4, ADC
36 crystals
2 SiPM/crystal
Fill one bin with 2 SiPMs data (after calibration?)
Numbers in red is average ADC
Emax
!Emax
Shower?
I still think the plot cab be better
Can you Draw->(“hits”)?
Canvas->Divide(6, 6, 0, 0)
Increase the size of axis
same range of axis in x and y for all plots

## Slide 7: Raw Hit Distribution : PbWO4, ADC
36 crystals
2 SiPM/crystal
Fill one bin with 2 SiPMs data (after calibration?)
Numbers in red is average ADC
Emax
!Emax
Shower?
I still think the plot cab be better
Can you Draw->(“hits”)?
Canvas->Divide(6, 6, 0, 0)
Increase the size of axis
same range of axis in x and y for all plots
AFTER Cali

## Slide 8: Beam Monitor : Find Position by Coming Hits
BM1
BM2
Gravity-weighted method
, and wi = ADCi
Equal-weighted method
and wi =1
  ADCmax method
  ADCmax strip to define (X, Y)
All the events chosen are after timing matching between BMs and ZDC crystals.

## Slide 9: Find Position by Coming Hits : ADCmax
BM1
BM2
  ADCmax method
  ADCmax strip to define (X, Y)
  1D in X
  1D in Y

## Slide 10: Find Position by Coming Hits : ADC-weighted
BM1
BM2
  1D in X
  1D in Y
Gravity-weighted method
, and wi = ADCi

## Slide 11: Find Position by Coming Hits : Equal-weighted
BM1
BM2
  1D in X
  1D in Y
Equal-weighted method
and wi =1

## Slide 12: Position Correlation : BM is Equal-weighted
BM1 VS BM2
BM1 VS PbWO
BM2 VS PbWO
X
Y
BM is ADC
Before Cali.

## Slide 13: Position Correlation : BM is ADC-weighted
BM1 VS BM2
BM1 VS PbWO
BM2 VS PbWO
X
Y
BM is ADC
Before Cali.

## Slide 14: Position Correlation : BM is Equal-weighted
BM1 VS BM2
BM1 VS PbWO
BM2 VS PbWO
X
Y
BM is ADC
After Cali.

## Slide 15: Position Correlation : BM is ADC-weighted
BM1 VS BM2
BM1 VS PbWO
BM2 VS PbWO
X
Y
BM is ADC
After Cali.

## Slide 16: Position Resolution (Residual) BM is Equal Weighted
Residual in X and Y
Residual in R
Position assignment : Equal-weighted for BMs and gravity-weighted for PbWO4 crystal.
Position resolution
Since the resolution of BMs (2mm pitch) are very small compared PbWO4 crystal (2cm pitch), we can consider the resolution~8mm is mostly from PbWO4 crystal itself.
Sigma = 7.889 +/- 0.041 mm

## Slide 17: Position Resolution (Residual) BM is ADC Weighted
Residual in X and Y
Residual in R

## Slide 18: Clustering
Emax
E3x3
E5x5
Emax/E5x5
E3x3/E5x5

## Slide 19: Produce PDF files One energy for one PDF file

## Slide 20: Energy VS Energy Resolution (w/o regression)

## Slide 21: Energy VS Position Resolution

## Slide 22: Rayleigh Distribution

## Slide 24: Misalignment Effect

## Slide 25: Unsymmetrical Effect