## Slide 1: ZDC MC Simulation 20260112
Chia-Yu Hsieh
Academia Sinica, Taiwan

## Slide 2: Goal
Build up official MC framework (done)
Analysis MC output to get energy/position resolution (undergoing)
Test w/ event generators for pion and kaon structure study

## Slide 3: ECAL Versions
WSi Branch : https://github.com/alillari/epic-UConn-ZDC-WSi
There are 4 setting files for ECAL, one for crystal and 4 for WSi setup.
epic_zdc_lyso_sipm.xml : <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_Crystal_LYSOxml"/> epic_zdc_wsi_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_LG.xml"/>
epic_zdc_wsi_hg1_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_1.xml"/> epic_zdc_wsi_hg2_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_2.xml"/> epic_zdc_wsi_hg3_sipm.xml: <include ref="${DETECTOR_PATH}/compact/far_forward/ZDC_WSi_HG_3.xml"/>

## Slide 4: Official ZDC Design : Crystal ECAL + HCAL
ECAL
LYSO Crystal
20*20 cells
3cm*3cm*7cm / cell
60cm*60cm
7cm ~ 6.5X0 in Z
HCAL : sampling calorimeter
1 layer = steel + scintillator tile + SiPM
64 layers, 8 slice/layer
65cm in X, 60cm in Y, 163cm in Z
Beam line
ZDC = ECAL + HCAL

## Slide 5: ECAL Design (1)
LYSO Crystal
20*20 cells
3cm*3cm*7cm / cell
60cm*60cm
7cm ~ 6.5X0 in Z
Crystal ECAL (epic_zdc_lyso_sipm.xml)
20 pad layer, No pixel layer
20 layers “PAD” Wsi (no Pixel layer)
1 layer = W (3.5mm) + glue (0.11um, G10) + Si pad (320mm, Si) + glue (0.11um, G10) + PCB (1.6mm, PET) + Air (1mm)
Si pad = 1cm*1cm => 60 pads / layer
  Wsi w/ low granularity (epic_zdc_wsi_sipm.xml)

## Slide 6: ECAL Design (2)
WSi w/ high granuarity1 (epic_zdc_wsi_hg1_sipm.xml) 17 pad + 3 pixel (3, 6, 9)
WSi w/ high granuarity2 (epic_zdc_wsi_hg2_sipm.xml) : 17 pad + 3 pixel (4, 8, 12)
WSi w/ high granuarity2 (epic_zdc_wsi_hg3_sipm.xml) 17 pad + 3 pixel (5, 10, 15)
20 layer = 17 layers “PAD” Si + 3 layer “Pixel” Si
1 layer = W (3.5mm) + glue (0.11um, G10) + Si pad/pixel (320mm/300mm, Si) + glue (0.11um, G10) + PCB (1.6mm, PET) + Air (1mm)
Si pad : 1cm*1cm, 3600 pads / layer
Si pixel : 0.5mm* 0.5mm, 1,440,000 pixel / layer

## Slide 7: Analyze MC to get energy resolution
Crystal ECAL + Sampling HCAL
Code mainly developed by Shima and Po-Ju

## Slide 8: Relocate Detector and Beam Position
Put detector straight along z-dir
Shoot beam to center of ZDC crystal (shift 15mm in both x and y directions)
1GeV-40GeV gamma pencil beams shoot to the center of crystal and the detector is put straight in order to simplify the case.

## Slide 9: Energy Dump
Before energy regression
After energy regression (linear regression, 1 = p0 + p1*ECAL + p2*HCAL)
ECAL
HCAL
ECAL + HCAL
ECAL
HCAL
ECAL + HCAL

## Slide 10: Fit Reconstructed Energy
Double-side crystal ball fit

## Slide 11: Energy Resolution for Gamma
LYSO-crystal ECAL+ Sampling Calorimeter HCAL
=> Satisfy the energy resolution requirement.
1GeV-40GeV gamma pencil beams

## Slide 12: Analyze MC to get position resolution
Crystal ECAL + Sampling HCAL

## Slide 13: Strategy to Access Position Resolution
MC truth is simple and expected since pencil beam is shouted @ (-15mm, -15mm, z)
Particle tracking :
layer by layer define a weighted position
(ECAL=1 layer, HCAL = 64 layers)
Fit 64 layers by polynomial1
(only HCAL is used in tracking now)
Evaluate residual (trackPos-MCPos)
Position resolution = sigma of gaussian fit of residual
Use 40GeV gamma sample to test

## Slide 14: Hit Distribution of ECAL (1000 evts)
Hit position in X
=> 20 peaks/crystals
Hit position in Y
=> 20 peaks /crystals
Hit position in Z
=> 1 peak
Weighted pos in X
=> Centered ~ -15mm
Weighted pos in Y
=> Centered ~ -15mm
Weighted pos in Z
Hit multiplicity
~ 100 hits/evt

## Slide 15: Hit Distribution of HCAL (1000 evts)
Hit position in X
=> 28 peaks
Hit position in Y
=> 49 peaks
Hit position in Z
=> 64 peak/layers
Weighted pos in X
Centered ~ -24mm(?)
Weighted pos in Y
=> Centered ~ -15mm
Weighted pos in Z
=> Peak @ 7th layer
Hit multiplicity
~ 200 hits/evt

## Slide 16: ECAL : Hits in XZ and YZ (evt#0)
Raw hit position (color is Edmp)
Energy-weighted hit position

## Slide 17: HCAL : Hits in XY (evt#0)
Center is more energy dump
Not many hits after layer#20

## Slide 18: HCAL : Fit pol1 (evt#0)
Raw hits (color weighted by Edmp)
Energy-weighted hit position
Tracking on xz plane
(not along beam?)
Tracking on yz plane
(ok)

## Slide 19: Residual @ Weighted-Z position (Only HCAL Included in Track Reconstruction)
With HCAL along, 40GeV gamma pencil beam, position resolution ~ 2.7mm

## Slide 20: Position Resolution and Shift
Energy (GeV) | Sigma X(mm) | Sigma Y(mm)
0.7 | 21.79 | 17.25
1.0 | 16.28 | 15.29
3 | 6.87 | 6.67
5 | 5.86 | 5.01
7 | 6.72 | 5.62
9 | 5.03 | 4.18
10 | 4.68 | 3.56
20 | 3.64 | 3.06
30 | 2.82 | 2.83
40 | 2.62 | 2.75
Energy (GeV) | Mean X (mm) | Mean Y (mm)
0.7 | −13.50 | +0.17
1.0 | −10.53 | +0.68
3 | −12.06 | −0.53
5 | −11.97 | −0.68
7 | −9.26 | +1.01
9 | −9.83 | +0.24
10 | −10.40 | −0.14
20 | −8.55 | +0.17
30 | −8.65 | −0.09
40 | −8.46 | −0.07
Position resolution in Y is better than X in low energy.

## Slide 21: Track Reconstruction is Difficult for Low Energy Beam
40GeV Gamma
300 GeV neutron
1 GeV neutron
0.7 GeV Gamma
For neutron, energy~ 1GeV, shower is quite spread.
For gamma, energy<0.5GeV, barely hits in HCAL.

## Slide 22: Neutron Beam Pencil @ (-15, -15, z) {10, 20, 50, 100, 200, 300} GeV

## Slide 23: Energy Dump
Energy dump BEFORE energy regression
Energy Dump AFTER energy regression
(linear regression, y = p0 + p1*ECAL + p2*HCAL)
ECAL
HCAL
ECAL + HCAL
ECAL
HCAL
Leak
ECAL
+ HCAL
+ Leak
Energy not well reconstructed for neutron<50GeV
2%-6%
1.5 %

## Slide 24: Energy Regression/Resolution
10 GeV
20 GeV
50 GeV
100 GeV
200 GeV
300 GeV
Energy resolution, ok!

## Slide 25: Nhits VS Energy (1 fill = 1 per Layer, 1000 evts)
10 GeV neutron
20 GeV neutron
50 GeV neutron
100 GeV neutron
200 GeV neutron
300 GeV neutron
Lower energy, less hits and less energy left in HCAL

## Slide 26: Track Reconstruction (evt#0, XZ)
10 GeV neutron
20 GeV neutron
50 GeV neutron
100 GeV neutron
200 GeV neutron
300 GeV neutron
Bad track reconstruction for low energy beam. => apply some cuts on energy or Nhits? Or weight higher energy layer more in tracking?

## Slide 27: Track Reconstruction (evt#0, YZ)
10 GeV neutron
20 GeV neutron
50 GeV neutron
100 GeV neutron
200 GeV neutron
300 GeV neutron

## Slide 28: Residual Layer by Layer @ 1GeV
@XZ

## Slide 29: Residual Layer by Layer @ 300GeV
@XZ

## Slide 30: Residual @ Weighted-Z, XZ Plan
10 GeV neutron
20 GeV neutron
50 GeV neutron
100 GeV neutron
200 GeV neutron
300 GeV neutron

## Slide 31: Residual @ Weighted-Z, YZ Plan
10 GeV neutron
20 GeV neutron
50 GeV neutron
100 GeV neutron
200 GeV neutron
300 GeV neutron

## Slide 32: Mean (Bias) and Sigma (Position Resolution) of Residual
Energy (GeV) | meanX (XZ) | sigmaX (XZ) | meanY (YZ) | sigmaY (YZ)
10 | −8.65 | 21.79 | +0.80 | 17.71
20 | +0.32 | 16.79 | +0.16 | 15.79
50 | −0.20 | 13.88 | +0.64 | 13.44
100 | +0.65 | 8.45 | +0.60 | 8.70
200 | +0.77 | 5.66 | +0.56 | 5.66
300 | +0.89 | 4.85 | +0.86 | 4.86
No shift in X anymore, unlike gamma beam.
=> problem is low energy dump in HCAL and mostly in ECAL?
Higher beam energy=> better position resolution.

## Slide 33: Mean (Bias) and Sigma (Position Resolution) of Residual