## Slide 1: Weekly meeting
Yu-Siang Xiao (蕭宇翔)
2026 03/13

## Slide 2: The cosmic ray test(last week)
Finish the configuration of the Cosmic ray runs for the program, which like the channels mapping, the drawing mapping/ setting…
Finish the test of reconstructing the event by detectors.
Keep going on the ADC cut(offline threshold), and the algorithm development for the full readout mode.

## Slide 3: Cosmic ray event reconstruction
Using the data from 2026/01/01 to 2026/02/25.
Total data taking time in data set = 31 days
According to the geometry and flux calculation of muon, we may take 645 event per day.
The event count will be use the operation time to get the normalized histogram.
The 2/14 ,2/20~2/22 have some problem, with too much event!

## Slide 4: Cosmic ray data ADC1x1, E1x1
The peak of ADC1x1 is ~21463 ADC.
  PS: The channel didn’t do the gain calibration in program, yet.
According to the E = (ADC-771)/281.72:
  21463 ADC~73.45 MeV which is approach the MIP value.
    MIP(6X0 PbWO4, 3GeV)~82.75MeV
Zoom in

## Slide 5: The DAQ cut issue
1. Not fire channel ADC
2. Fire channel ADC
3. ADC VS fire Eff.(fire cnt./(fire+!fire) cnt.)
4. ROC curve during scan the ADC.
5. The best cut(ADC) value for distinguish the ADC value is fire of not.
6. The raw data multiplicity(separate the ROC).
PS: the ROC curve depends on:
  Suppose the fire signal is real signal.
  Assuming the !fire is noise contribute by full readout.
Best cut point: max(Youden's Index)
  to be max value.

## Slide 6: The DAQ cut BM 2 – X(1st layer)
Some 16 channel is more easier to be fire than other channels.

## Slide 7: The DAQ cut BM 2 – Y(2nd layer)
The channels is more uniform than X plane.

## Slide 8: The DAQ cut PbWO4– ROCA(4th layer)
A larger dynamic range(MIP).
The multiplicity has a 16 hits peak, means maybe some noise make the half channels fire. It’s also tell use the DAQ cut is not the best.

## Slide 9: The DAQ cut PbWO4– ROCB(4th layer)
A larger dynamic range(MIP).
Same as the ROCA, but the nHits shows the DAQ cut is more less to make all of the channel fire by the noise together(nHits=32).

## Slide 10: The DAQ cut BM 1 – X(5rd layer)
Don’t know why the signal have a large separation, when we compare to the BM2.

## Slide 11: The DAQ cut BM 1 – Y(6th layer)
Sama situation as BM1 X plane.
But the channel feature is more uniform than X plane.

## Slide 12: Apply the best ADC cut value on matching data.
Take PbWO4 data for example:
The new cut make the raw data look better.
  ROC A: The peak (nHits=16) become flat.
    Could mean the signal is not large enough could be calculate in containment.
  ROC A&B: The peak (nHits=2) is lower.
    The event which is the single crystal under high cut could be solve.
ROCA
Best cut
ROCB
Best cut
Best cut

## Slide 13: The GADC11 after cut
The fitting peak of MIP: 21463->21878 ADC, 73.5-> 74.9 MeV, Sigma: 25.9->22.1MeV
The = 2.10->0.82(over fitting because the parameter is too much to fit the best cut data.)
Best cut

## Slide 14: The cosmic ray moun analysis to do
Remove the data from Feb. 14~24(the low THR cause higher event rate, and matching rate).
  PS: the high fire rate noise should not increase too much event like the data.
Using the best cut result data to do the reconstruction and selection of timing matching data.

## Slide 15: ZDC EMCal Design
The EMCal is shown with the following specifications:
PbWO4 crystal array：
  Crystal size 20.5 mm × 20.5 mm × 6X0
  Allow an additional ~0.5mm for the reflector and crystal wrapping
  One Super Module (SM)：9 × 9 crystals
  Allow 1mm of stainless for the SM wrapping.
  SM size : (21.0×9+2)2 cm2
  Full array: 3x3 SM = (3×191)2 cm2
  Total number of crystal modules： 3x3x3x3 = 729
SiPM： S14160-3015PS_HAMAMATSU
  16 MPPC channels for each crystal
  Total number of MPPC channels： 11,664
Support and Cooling design： aluminum + copper tube
  Use a 13mm thick aluminum plate
  Coolant is circulated through copper tubing.
Cable routing：
  The cables go downward and pass through the table
20 cm
80 cm
60 cm
60 cm
6 cm
Super Module readout hubs

## Slide 16: Supper Module
One SM contains :
  9 × 9 PbWO4 crystals
  16 × 9 × 9 SiPM channels = 1,296 channels
Zoom in

## Slide 17: SiPM Readout Module
Readout module
1
The current design contains 3 × 3 readout modules per Super Module
One readout module contains :
  144 MPPC channels
  2 ROCs
  Thermal contact
3 × 3 = 9 crystals (reduce the display size by 75%)
(4×4)×3×3 = 144 MPPCs
SiPM module readout board
SiPM module readout board
2 ROCs: (72 × 2=144 channels)
HV, GND, and Signal
cables
63 cm
63 cm
1 Super Module

## Slide 18: Cooling & Support System
Use 4 cooling modules to collect the heat from SiPMs
The coolant circulates through copper tubing

## Slide 19: Mass Calculation
Super module： 16.4 kg
Cooling support： 4.2 kg
Total ： 16.4 × 9 + 4.2 = 151.8 kg
Cables and PCBs have not yet been included in the calculation
184.6 g
16405.3 g

## Slide 20: End

## Slide 21: backup

## Slide 22: MIP Calculation
Bethe-Bloch Eq. :
=
Total energy loss: * interaction length()
MIP