## Slide 1: Weekly meeting
Yu-Siang Xiao (蕭宇翔)
2026 03/13

## Slide 2: The cosmic ray test(last week)
Finish the configuration of the Cosmic ray runs for the program, which like the channels mapping, the drawing mapping/ setting…
Finish the test of reconstructing the event by detectors.
Keep going on the ADC cut(offline threshold), and the algorithm development for the full readout mode.

## Slide 3: Cosmic ray event reconstruction
Using the data from 2026/01/01 to 2026/02/25.
Total data taking time in data set = 31 days
The “count of event” come from matching.
According to the geometry and flux calculation of muon, we may take 645 event per day.
Now, I remove the high rate data: Feb14~Feb24.
And do the tracking by the “Hit” channel which identify by “DAQ” system.
remove

## Slide 4: The GADC11 after cut
Removing the abnormal data make the spectrum clearly than before.
Not apply the analysis cut and gain calibration, yet.
Filt Data

## Slide 5: The tracking process & residual
The star marker means the Center Of Gravity(COG) of layers.
BM1 layer
BM2 layer
PbWO layer
Track
Interpolate predict
PbWO COG
BM2 COG
BM1 COG
Residual
Hit ID for BM1 X
Without ID BM1 X
Hit ID for BM2 X
Without ID BM2 X
Without ID BM1 Y
Hit ID BM1 Y
Without ID BM1 Y
Hit ID BM2 Y
Without ID PbWO
Hit ID PbWO
Interpolate of BM COGs = track and predict.
Residual = COG - Interpolate predict

## Slide 6: Apply the tracking cut to filter the noise
Do the Gain calibration of channel by JP BT config.
Has track: the event pass detector2,3,4 (2 BM+PbWO4).
nH2 A&B<=3: Number of fire hit on each BM1 layer <=3.
nH3 A&B<=3: Number of fire hit on each BM2 layer <=3.
nCry = 1: Number of fire crystal on PbWO only 1.
Emax > 0: filter the noise.
|Δ| cut = residual cut.
BM1 layer
BM2 layer
PbWO layer
Residual
The cut means:
  Low nHits on BM = accurate track, no shower.
  Single crystal cut: no share, shower.
  |Δ| cut: precision of track.

## Slide 7: The Emax after the cut
Try 3 range for |Δ|, >10, <10, >25. The |Δ|<10 have a little different between the other case, which is sharper between 2 peaks.
|Δ|
Track θ

## Slide 8: The Emax after the cut(fit)
Using Gaussian tail to fit the lower energy spectrum, and gaussian to fit the MIP.
The |Δ| < 10 is more reasonable and have a better fit.
|Δ| > 10
|Δ| < 10
The fitting shows the of golden events MIP = 55.89(2.02)MeV.

## Slide 9: The Emax after the cut(fit)
Using Gaussian tail to fit the lower energy spectrum, and gaussian to fit the MIP.
The |Δ| < 10 is more reasonable and have a better fit.
|Δ| < 10
The fitting shows the of golden events MIP = 55.89(2.02)MeV.
MC

## Slide 10: The Emax after the cut(fit)
Using Gaussian tail to fit the lower energy spectrum, and gaussian to fit the MIP.
The |Δ| < 10 is more reasonable and have a better fit.
|Δ| < 10
The fitting shows the of golden events MIP = 55.89(2.02)MeV.
MC
~57MeV

## Slide 11: Why the spectrum contains 2 peak in ADC
The lower ADC peak ~ 40~50%(1K ADC/2K ADC) ADC of MIP peak Could because:
  Emax crystal only fire 1 channel. => In this cases, nHits PbWO4 = 1 & nCrys = 1.
  Two crystals share the MIP. => nCrys = 2 or large θ pass 2 crystal.
  2 crystal share energy on different ROC but 1 ROC no data. => check track not on the boundary of ROCs.

## Slide 12: Emax crystal only fire 1 channel.
Previous cuts:
  has track, nHs of BM x/y layers <=3, and Emax > 0MeV
Using selection: nHits PbWO4 = 1 or 2 to do comparision.
It’s appearance that no more event in this case.
No way by this reason! Which only fire 1 channel in the only crystal.

## Slide 13: Two crystals share the MIP.
Previous cuts:
  has track, nHs of BM x/y layers <=3, and Emax > 0MeV.
Case cut : nCrys PbWO4 = 1 or 2 and fire all channel.
In the Emax, the 2 crystal is surely to share the MIP energy.
The peak is lower than MIP.
The θ distribution is wider!
But isn’t contribute on lower energy tail.

## Slide 14: Two crystal share energy on different ROC but 1 ROC no data
Previous cuts:
  has track, nHs of BM x/y layers <=3, and Emax > 0MeV.
Case cut : check if the Emax crystal at the boundary or not.
  Abs(COG Y)<12mm: center 2 row crystals.
  >12mm: outer 2 rows.
The spectrum has no more change on the lower peak.

## Slide 15: Why the spectrum contains 2 peak in ADC
The lower ADC peak ~ 40~50%(1K ADC/2K ADC) ADC of MIP peak Could because:
  Emax crystal only fire 1 channel. => In this cases, nHits PbWO4 = 1 & nCrys = 1.
  Two crystals share the MIP. => nCrys = 2 or large θ pass 2 crystal.
  2 crystal share energy on different ROC but 1 ROC no data. => check track not on the boundary of ROCs.
Still don’t know why the MIP selection contain a lots the half ADC event.

## Slide 16: Apply the best ADC cut value on matching data.
Take PbWO4 data for example:
The new cut make the raw data look better.
  ROC A: The peak (nHits=16) become flat.
    Could mean the signal is not large enough could be calculate in containment.
  ROC A&B: The peak (nHits=2) is lower.
    The event which is the single crystal under high cut could be solve.
ROCA
Best cut
ROCB
Best cut
Best cut
Last week nHits problem:
Why nHits of 1 ROC often to be 16? Has any rule?

## Slide 17: Ask of the nHits = 16 question
I take the BM2 for nHits of ROC A and B both equal 16, the fire channels occupy the odd or even channels.
The BM1 ROCB even fire all channels.

## Slide 18: The cosmic ray moun analysis to do
Remove the data from Feb. 14~24(the low THR cause higher event rate, and matching rate).
  PS: the high fire rate noise should not increase too much event like the data.
Trying the best cut result data to do the reconstruction and selection of timing matching data.

## Slide 19: ZDC EMCal Design
The EMCal is shown with the following specifications:
PbWO4 crystal array：
  Crystal size 20.5 mm × 20.5 mm × 6X0
  Allow an additional ~0.5mm for the reflector and crystal wrapping
  One Super Module (SM)：9 × 9 crystals
  Allow 1mm of stainless for the SM wrapping.
  SM size : (21.0×9+2)2 cm2
  Full array: 3x3 SM = (3×191)2 cm2
  Total number of crystal modules： 3x3x3x3 = 729
SiPM： S14160-3015PS_HAMAMATSU
  16 MPPC channels for each crystal
  Total number of MPPC channels： 11,664
Support and Cooling design： aluminum + copper tube
  Use a 13mm thick aluminum plate
  Coolant is circulated through copper tubing.
Cable routing：
  The cables go downward and pass through the table
20 cm
80 cm
60 cm
60 cm
6 cm
Super Module readout hubs

## Slide 20: Supper Module
One SM contains :
  9 × 9 PbWO4 crystals
  16 × 9 × 9 SiPM channels = 1,296 channels
Zoom in

## Slide 21: SiPM Readout Module
Readout module
1
The current design contains 3 × 3 readout modules per Super Module
One readout module contains :
  144 MPPC channels
  2 ROCs
  Thermal contact
3 × 3 = 9 crystals
(4×4)×3×3 = 144 MPPCs
(reduce the display chips by 75%)
MPPC board
MPPC ROC board
2 ROCs: (72 × 2=144 channels)
HV, GND, and Signal
cables
63 cm
63 cm
1 Super Module

## Slide 22: The readout module boards
High-Density Integration: Accommodates 144 MPPC sensors within a compact 63 × 63 mm.
Dual-Layer PCB Stack:
  MPPC Board (Front): Dedicated to photon detection and signal interface with the crystal array.
  ROC Board (Back): Equipped with two Readout Chips (ROCs) for signal processing and digitization.
Interconnect & Connectivity
  Board-to-Board (B2B) Connector:
  Utilizes an 8 mm standoff height.
  Benefit: Minimizes analog trace length between sensors and ROCs to ensure signal integrity and low noise.
  External Cabling:
  Features three robust rear-exit cables for High Voltage (HV) bias and high-speed data transmission.

## Slide 23: Cooling & Support System
Use 4 cooling modules to collect the heat from SiPMs
The coolant circulates through copper tubing

## Slide 24: Mass Calculation
Super module： 16.4 kg
Cooling support： 4.2 kg
Total ： 16.4 × 9 + 4.2 = 151.8 kg
Cables and PCBs have not yet been included in the calculation
184.6 g
16405.3 g

## Slide 25: End

## Slide 26: backup

## Slide 27: MIP Calculation
Bethe-Bloch Eq. :
=
Total energy loss: * interaction length()
MIP