## Slide 1: EPIC ZDC EMCal design
Yu-Siang Xiao (蕭宇翔)
2026 04/01

## Slide 2: ZDC EMCal Design
90
59
59
8.87
45
39
Unit: cm
88
6
6
6
170
Maintenance position
Operation position
stage
EMCal
Readout hubs
2.5
The EMCal is shown with the following specifications:
PbWO4 crystal array：
  Crystal size 20.5 mm × 20.5 mm × 7.0 mm (7.87 X0 )
  Allow an additional ~0.5mm for the reflector and crystal wrapping
  One Super Module (SM)：9 × 9 crystals
  Allow 1mm of stainless for the SM wrapping.
  SM size : (21.0×9+2)2 cm2
  Full array: 3x3 SM = (3×191)2 cm2
  Total number of crystal modules： 3x3x3x3 = 729
SiPM： S14160-3015PS_HAMAMATSU
  16 MPPC channels for each crystal
  Total number of MPPC channels： 11,664
Support and Cooling design: Aluminum + copper tube + copper board.
  Side part: Use 8 mm thick aluminum plates
    Coolant is circulated through copper tubing in aluminum plates .
  Front part: Cover by a 3 mm copper plate.
Cable routing：
  The cables go downward and pass through the table
  Max length ~ 95 cm
p/A beam pipe

## Slide 3: Supper Module
One SM contains :
  9 × 9 PbWO4 crystals
  16 × 9 × 9 SiPM channels = 1,296 channels
Zoom in

## Slide 4: The compose system of EMCal
Cooling & support
This is the assemble sequence.
1. The Cooling & support
2. The crystal modules
3. PCB support frame
4. The sensor and ROC board, and the cables.
Crystal modules
PCB support
ROC & SiPM PCB

## Slide 5: SiPM Readout Module
Readout module
1
The current design contains 3 × 3 readout modules per Super Module
One readout module contains :
  144 SiPM channels
  2 ROCs
  Thermal contact
3 × 3 = 9 crystals
(4×4)×3×3 = 144 SiPMs
(reduce the display chips by 75%)
SiPM board
ROC board
2 ROCs: (72 × 2=144 channels)
HV, GND, and Signal
cables
19.1 cm
19.1cm
1 Super Module

## Slide 6: The readout module boards
High-Density Integration: Accommodates 144 SiPM sensors within a compact 63 × 63 mm.
Dual-Layer PCB Stack:
  SiPM Board (Front): Dedicated to photon detection and signal interface with the crystal array.
  ROC Board (Back): Equipped with two Readout Chips (ROCs) for signal processing and digitization.
Interconnect & Connectivity
  Board-to-Board (B2B) Connector:
  Utilizes an 8 mm standoff height.
  Benefit: Minimizes analog trace length between sensors and ROCs to ensure signal integrity and low noise.
  External Cabling:
  Features three robust rear-exit cables for High Voltage (HV) bias and high-speed data transmission.
SiPM
SiPM

## Slide 7: Cooling & Support System
Use 1 cooling modules, 4 cooling support, and 3mm copper plate to maintain the thermal condition of crystals.
The coolant circulates through 6mm copper tubing.
1x
4x
Assemble
Copper plate
T=3 mm
Cooling support

## Slide 8: Mass Calculation
Super module：21.1 kg, and SM x 9：190.3 kg
Cooling system：12.1 kg
PCB support frame：3.6 kg
PCB of ROC and SiPM：3.5 kg
Total ： 209.5 kg
Super module

## Slide 9: Energy resolution