## Slide 1: 7/29 Report

## Slide 2: RPC Testing
When the trigger detects a cosmic ray, the oscilloscope records the signal from the RPC.
trigger
RPC

## Slide 3: Signal Search
Signal detected: Using the moving average to filter noise, find the signal.
Moving average:
If there is value over in any RPC channel, it would be considered as an event.

## Slide 4: Signal Search
Calculate the voltage-value distribution before 70 ns and determine the fifth standard-deviation threshold.
Any value exceeding this threshold is identified as an event .

## Slide 5: RPC Efficiency
Measure channels
Applied voltagev | Efficiency (Moving avg) | Efficiency (Sigma)
10 kV | 4% | 3%
11kV | 1% | 2%
12kV | 7% | 7%
13kV | 14% | 30%
14kV | 59% | 83%
15kV | 83% | 95%

## Slide 6: RPC Efficiency
Measure channels
Applied voltage | Efficiency (Moving avg) | Efficiency (Sigma)
10 kV | 1% | 0%
11kV | 0% | 3%
12kV | 1% | 3%
13kV | 1% | 26%
14kV | 15% | 54%
15kV | 28% | 53%

## Slide 7: RPC Efficiency
Measure channels
Applied voltage | Efficiency (Moving avg) | Efficiency (Sigma)
10 kV | 0% | 1%
11kV | 0% | 6%
12kV | 2% | 8%
13kV | 12% | 32%
14kV | 27% | 56%
15kV | 46% | 84%

## Slide 8
Applied voltage | Efficiency (Moving avg) | Efficiency (Sigma)
10 kV | 1% | 0%
11kV | 0% | 3%
12kV | 1% | 3%
13kV | 1% | 26%
14kV | 15% | 54%
15kV | 28% | 53%
Applied voltage | Efficiency (Moving avg) | Efficiency (Sigma)
10 kV | 0% | 1%
11kV | 0% | 6%
12kV | 2% | 8%
13kV | 12% | 32%
14kV | 27% | 56%
15kV | 46% | 84%
Applied voltage | Efficiency (Moving avg) | Efficiency (Sigma)
10 kV | 4% | 3%
11kV | 1% | 2%
12kV | 7% | 7%
13kV | 14% | 30%
14kV | 59% | 83%
15kV | 83% | 95%