## Slide 1: RPC work
Chia-Yu Hsieh
Academia Sinica, Taiwan

## Slide 2: RPC Electronics for JP
Amp production
30 pcs ready
220 pcs under production
Discriminator control code
python-based code is ready by濂宸
problem with setting threshold board by board
Dr. Chu is investigating
Discriminator prototypes (test beam in Oct. 2026)
Dis#1 : change polarity, 2026_v1, 3 boards produced, test beam in Oct.
Dis#2 : change polarity + more stretcher, Dr. Chu still designing
Dis#3 : positive signal, same board as Dis#1 but remove/add capacitors

## Slide 3: Review Carbonless RPC (1)
https://www.sciencedirect.com/science/article/pii/S0168900225005698

## Slide 4: Review Carbonless RPC (2)

## Slide 5: Review Carbonless RPC (3)
Increase the thickness of
FR4 layer

## Slide 6: New Carbonless PCB
A
B
C
Increase the thickness of FR4
Change the size of pad : change of size of clustering => change the size of signal?

## Slide 7: Carbonless : Study with Oscilloscope
翊銘 : please report this study, Eff and signal ADC
Do we have everything to setup this in NCU?
Carbonless
Scin_top
Scin_bottom
AND
Amp
Oscilloscope
Trigger
res~ns
signal
LV +6V
HV +1kV
HV +1kV
HV = +7kV
+ HV= -7kV

## Slide 8: Carbonless : Efficiency and Time Resolution Study
Carbonless
Scin_top
Scin_bottom
AND
Amp
TDC
Trigger
signal#1
LV +6V
HV +1kV
HV +1kV
HV = +7kV
+ HV= -7kV
Carbonless
Amp
signal#2
@Trigger
matching
mode
翊銘 : please report this study, TDC control
Do we have everything to setup this in NCU?

## Slide 9: CEAN TDC test
Fun gen
Fan out
trigger
(TTL)
Dis.
(thres. = 100mV)
TDC
(0) trigger matching mode
win. Offset = 0 us
Win. window = 10us
signal
(TTL)
signal
(LVDS)

## Slide 10: To Do
翊銘
Study operation principle of RPC
Check modules (w/ 彥震)
Report carbonless work during summer
Test TDC again with better signal input?
濂宸
Prepare document for Spring8 test beam