## Slide 1: Weekly meeting
Yu-Siang Xiao (蕭宇翔)
2026 08/06

## Slide 2: GADC11 THR CUT
VF650 ~ 會讓EMAX<10K的數據掉資料，高能量約在20K以上不會掉資料換句話說，兩頻道都不會被CUT 影響的範圍約在2x 10K = 20k以上:
Condition: Emax 單晶片還是雙晶片觸發
197MeV
796MeV
因此進行MC-DATA 能量重建應由雙晶片觸發事件來決斷，使用該事件類別的
  DATA(ADC)-2OFF = MC(MeV) * GAIN
  MeV *GAIN+2OFF = ADC

## Slide 3: MC能量
已知MC能量@796 ~ 450MeV， DATA結果應相似
由於MC 只存晶體能量，不存SIPM光訊號，因此需要人為將訊號分成兩半

## Slide 4: DATA 觀察雙晶片能量比例
觀察 頻道34/40(主晶體)的晶片收到的訊號強度可以觀察到前面說的20kADC問題(上列的圖)
觀察晶片頻道34/40比例變化(下列的圖) 可以觀察到頻道之間還是有些微的增益差距(模擬告訴我們需要一樣)
98
197
796

## Slide 5: 兩頻道間的差距放到模擬裡面
將兩頻道的差距放進模擬裡面有助於同步DATA/MC低能量時由於個別CUT不同對E1x1的影響
  Gain Ratio = -0.05dB = 0.9885x
將比值分布(寬度)放進MC當中有助於讓MC有更接近DATA的解析度
  Signal fluctuation width = 0.45dB = 1.1092x

## Slide 6: (1st BT)The beam monitor angular result problem
The finite strip pitch and the spatial separation distance between the Beam Monitors impose an intrinsic single-strip geometric tracking limit of approximately on the system's angular resolution ceiling.
Based on Multiple Coulomb Scattering (MCS) theory, the mean scattering angle scales inversely with momentum at low energies, which convolutes with the constant tracking resolution floor across the scanned energy spectrum.
Refinement: By incorporating theoretical predictions and physical parameters, I developed a comprehensive geometric fitting formula.
Result: The new fit model perfectly aligns with experimental observations, fully explaining the data across all energy ranges.