## Slide 1: ECal 3rd Prototype Beam Test Analysis
Yen-Chen Wu
Dept. Physics, National Central University
2026/08/14

## Slide 2: Energy Resolution Analysis Approach
ADC raw max
ADC max after fitting
ADC waveform integration
TOT
TOA
check resolution of E1x1, E3x3, E4x4, E1x1/E3x3, E1x1/E4x4, E3x3/E4x4 with all variables to find the one give the best resolution
apply different cut, TOT, TOA, event matching to see if resolution improved

## Slide 3: Target run
Energy resolution of:
1 X 1,
3 X 3,
crystal clustering
will be studied
Run 421~434,481,482 @ HV=45V, C=0xA
Positron beam shoot at Crystal 7
Event selection need to be done with tracking from BM 3&4.
However, tracking requires event matching between BM and PbWO4 beforehand, which I will learn later.
My first try will not include tracking & event selection.
Crystal 7
Channel Mapping

## Slide 4: Crystal status overview
abnormal channels appear in same channel across different run
All channels have basically the same waveform pattern in the same event.
All channels in crystal#3,4,7,10,11 function well.
Problems:
dead channels are found in (exclude in later analysis) crystal#2 : 63, 40, 52, 42 (4 dead) crystal#6: 64, 45, 47, 49, 51 (5 dead) crystal#8: 173, 175 (2 dead) crystal#12: 284, 286, 231, 250 (4 dead)
Abnormal waveform pattern found in crystal#2,6,8,12
Those channels are simply excluded in the analysis
3 4
7
10 11
Well-function crystal

## Slide 5: ADC[0] distribution (Run#482)
Crystal#2:
Crystal#2 should be excluded
If we take the energy as “ADCmax-ADC[0]”

## Slide 6: Crystal#2 pedestal issue
Event#1
Event#2
Event#3
Event#4
Event#5
dead
dead
dead
dead
Adc[0]=0
Adc[0]=0
Adc[0]=0
Adc[0]=0
Adc[0]=0
Adc[0]=0
Exclude in the later Crystal#2

## Slide 7: Run#482 1x1 vs. 3x3
Small peaks found in both low ADC and high ADC
Crystal#7 1x1
Crystal#7 3x3
Histogram is filled by:
“raw ADCmax – ADC[0]” averaged over all well-function channels in one crystal
summation over all 3x3 crystal
Beam energy: 705MeV
Crystal#2 excluded
ADCmax – ADC[0] distribution

## Slide 8: Excluding Crystal#2 does not help
Again, the second peak is mostly contributed by two crystals.
Strangely, under the condition that crystal#7 must be the lightest, the second largest is always crystal#6
They are from different FPGA!!?
ADCmax – ADC[0] distribution

## Slide 9: Energy resolution, BeamE = 823MeV
Energy resolution: 20.2%0.5%
Run#421
Run#422
Energy resolution: 18.8%0.7%
ADCMax-ADC[0]
ADCMax-ADC[0]
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7

## Slide 10: Energy resolution, BeamE = 705MeV
ADCMax-ADC[0]
Energy resolution: 20.1%0.2%
Run#481
Run#482
Energy resolution: 20.1%0.3%
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7
ADCMax-ADC[0]

## Slide 11: Energy resolution, BeamE = 584MeV
Energy resolution: 16.5%0.2%
Run#423
Run#424
Energy resolution: 18.3%0.5%
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7
ADCMax-ADC[0]
ADCMax-ADC[0]

## Slide 12: Energy resolution, BeamE = 492MeV
Energy resolution: 18.9%0.2%
Run#425
Run#426
Energy resolution: 18.4%0.5%
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7
ADCMax-ADC[0]
ADCMax-ADC[0]

## Slide 13: Energy resolution, BeamE = 395MeV
Energy resolution: 19.5%0.2%
Run#427
Run#428
Energy resolution: 18.2%0.4%
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7
ADCMax-ADC[0]
ADCMax-ADC[0]

## Slide 14: Energy resolution, BeamE = 297MeV
Energy resolution: 18.5%0.3%
Run#429
Run#430
Energy resolution: 19.1%0.5%
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7
ADCMax-ADC[0]
ADCMax-ADC[0]

## Slide 15: Energy resolution, BeamE = 197MeV
Energy resolution: 14.2%0.3%
Run#431
Run#432
Energy resolution: 14.1%0.4%
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7
ADCMax-ADC[0]
ADCMax-ADC[0]

## Slide 16: Energy resolution, BeamE = 100MeV
Energy resolution: 15.8%0.7%
Run#433
Run#434
Energy resolution: 14.9%0.5%
3x3 clustering around Crystal#7
Crystal#2 excluded
Dead channels excluded
3x3 clustering around Crystal#7
ADCMax-ADC[0]
ADCMax-ADC[0]

## Slide 17: Energy resolution vs. beam energy
Resolution =
TO DO:
Fit the original ADC waveform and define the pedestal

## Slide 18: ADCMax-ADC[0] 3x3 resolution
ADCMax-ADC[0]
For every beam E, there are two run

## Slide 19: Raw ADCMax 3x3 resolution
For every beam E, there are two run

## Slide 20: Energy resolution vs. beam energy
Resolution =
Next Step:
Fit the original ADC waveform and define the pedestal
tracking
ADCmax – ADC[0]
Raw ADCmax – pedestal max mean(constant)
By assuming ADC[0] is pedestal, better resolution is obtained from ADCMax-ADC[0] distribution.

## Slide 21: TO DO
The events in root file were not correctly decoded.
In some events, crystals given by FPGA1 and FPGA2 were not matched together on the correct timing, namely, signal from different events accidentally appear together.
The second peak observed in crystal#7 3x3 clustering energy distribution are contributed by crystal#6 &7 simultaneously, however, in reality, they should actually have come from different events.
Previous analysis on the energy resolution thus need to be redo on the correctly decoded data.
FPGA1 FPGA2
2 3 4
6 7 8
10 11 12