## Slide 1: RPC work
Chia-Yu Hsieh
Academia Sinica, Taiwan

## Slide 2: RPC Electronics for JP
Amp production
30 pcs ready
220 pcs under production (waiting for the import of components)
Discriminator control code
python-based code is ready by濂宸
problem with setting threshold board by board
Discriminator prototypes (test beam from Oct. 31st to Nov. 4th. 2026)
discriminator code and python firmware
(deadline : 10/16, two weeks for us to test)
discriminator production for positive signal
(deadline for design : 10/1, require 1 month for production)
discriminator production for new stretcher
(deadline for design : 10/1, require 1 month for production)
Student : 彥震

## Slide 3: Carbonless : Study with Oscilloscope
Setup finished
But HV tripped often => students report
Efficiency low? need to enlarger trigger size? Make new scintillator bar?
Carbonless
Scin_top
Scin_bottom
AND
Amp
Oscilloscope
Trigger
res~ns
signal
LV +6V
HV +1kV
HV +1kV
HV = +7kV
+ HV= -7kV

## Slide 4: Carbonless : Efficiency and Time Resolution Study
Carbonless
Scin_top
Scin_bottom
AND
Amp
TDC
Trigger
signal#1
LV +6V
HV +1kV
HV +1kV
HV = +7kV
+ HV= -7kV
Carbonless
Amp
signal#2
@Trigger
matching
mode
Need to make new frame -> layout of carbonless PCB
Discriminator

## Slide 5: To Do
Students in NCU
Draw new design carbonless 3D frame
Setup HV UI, to monitor current
Swap HV polarity on HV module to check if the high current is caused by HV polarity or PCB itself. Stable current +HV = 0.2uA, -HV = 1.2uA.
There is always one channel give larger
Analysis :
separate time zone : signal time zone ,noise time zone
fill amplitude histogram
noise time zone define threshold
efficiency after threshold cut
Build HV box?
濂宸
Control program
Myself
prepare carbonless PCB layout
Install discriminator and practice threshold control