## Slide 1: Basic Idea
Consistency?
When checking the consistency, we check only statistic error, or also include the systematic error?
BLUE combine
Covariance matrix C_total = C_sat, C_sys1, C_sys2;
C_total not necessary to include all errors.
Combine mean = weighting is affected by C_total, if we think there are errors should not affect the weighting of the mean, we should not include it.
Combine error = use C_total
Add new systematics after combing
Size could be half of the difference between A and B
Or pull method can be involved (not used if we do it for now) -> if not enough statistics
A
C
B
Consistency?
yes
C+ sysNew
No
BLUE combine
BLUE combine + add new sys

## Slide 2: Road Map
LL_P01
LL_P02
LL_P08
…
LO_P01
LO_P02
LO_P08
…
LL
LO
xsc3D +/- stat +/- sysA
LL_P01_pV
LL_P01_pC
+/- sysP
LL_P02_pV
LL_P02_pC
…
LL_P08_pV
LL_P08_pC
LO_P01_pV
LO_P01_pC
LO_P02_pV
LO_P02_pC
…
LO_P08_pV
LO_P08_pC
P01
P02
+/- sysT
…
P08
xsc3D
+/- stat
+/- sysA
+/- sysP
+/- sysT
+/- sysW
Step1 : Combine purity (3D xsc)
Step2 :
Combine
Trigger
(3D xsc)
Step3 :
Combine
Period
(3D xsc)
xsc2D
xsc1D
+/- stat
+/- sysA
+/- sysP
+/- sysT
+/- sysW
Step4 : Integration
(3D->2D/1D)

## Slide 3
LL
LL_P09_pV
LL_P09_pC
LO
LO_P09_pV
LO_P09_pC
Final 3D
2D/1D

## Slide 4: Step0 : Add sys, Combine, and Integration
Check first consistency
Are the inputs consistent? If yes, combine directly with no extra systematic. If not, add a new systematic.
New systematic
half of the difference between the two inputs
(what we do for trigger and purity) (pull is not used for now)
correlation factors ρ
Every BLUE combine needs correlation factors ρ, one per uncertainty source
(stat, sysA = acceptance, sysP = purity, sysT = trigger, sysW = week).
ρ = 0 (minimum): errors add in quadrature.
ρ = 1 (maximum): errors add linearly (no gain from combining).
Integration needs ρ between kinematic bins.
Step | Combine what | Method | New systematic
1 Purity | pV and pC (same data) | Simple mean (force w = ½ for each) | sysP = ¦ xpV − xpC ¦ / 2
2 Trigger | LL and LO | BLUE | sysT = ¦ xLL − xLO ¦ / 2
3 Period | P01 … P08 | BLUE | sysW = 0 for now
4 Integration | 3D bins → xsc2D, xsc1D | Sum, with ρ between bins | none

## Slide 5: Step1 : Combine purity, and sysP
LL_P01
xpV ± σstat,pV ± σsysA,pV
LL_P01_pV
LL_P01_pC
+/2
Step1 : Combine purity, 3D, bin by bin
xpC ± σstat,pC ± σsysA,pC
x̄ ± σstat ± σsysA ± σsysP
Catrina and Vincent use the same data. BLUE is not suitable to combine.
take the simple mean of the two. (Force the weighting for combined mean and sys = ½)
Central value | x̄ = ( xpV + xpC ) / 2
stat, sysA (ρ = 1) | σstat = ( σstat,pV + σstat,pC ) / 2 σsysA = ( σsysA,pV + σsysA,pC ) / 2
New sysP | σsysP = ¦ xpV − xpC ¦ / 2, added after the combine (in quadrature)
Source | ρ | Reason
stat | 1 | xpV and xpC come from the same raw yield N and differ only by the purity scale factor (fpV vs fpC). No independent statistical information.
sysA | 1 | The acceptance systematic comes from a common source, independent of the purity method. Vincent and Catarina’s results carry the same sysA.

## Slide 6: Step2 : Combine trigger, and sysT
LL_P01
LO_P01
P01
xLL ± σstat,LL ± σsysA,LL ± σsysP,LL
xLO ± σstat,LO ± σsysA,LO ± σsysP,LO
x̄ ± σstat,comb ± σsysA,comb
± σsysP,comb ± σsysT
How to combine? Use BLUE to combine, not a simple mean
the weights depend on all the errors (stat and sys) and on their correlations.
Weights (BLUE) | wLL = ( σLO2 − cov ) / ( σLL2 + σLO2 − 2 cov ), wLO = 1 − wLL σLL2 = σstat,LL2 + σsysA,LL2 + σsysP,LL2 (same for LO) cov = ρsysP σsysP,LL σsysP,LO (the other ρ are 0)
combine mean | x̄ = wLL xLL + wLO xLO (weight by sta only or sta+sys, test both)
combined err | σk,comb2 = wLL2 σk,LL2 + wLO2 σk,LO2 + 2 wLL wLO ρk σk,LL σk,LO k = stat, sysA, sysP, same weights for each; total σcomb2 = Σk σk,comb2
New sysT | σsysT = ¦ xLL − xLO ¦ / 2 (added after the combine, in quadrature)
stat | 0 | The two triggers are mutually exclusive: no event fires both, so no shared events.
sysA | ~0.8 0 | Same MC production (correlated) but different parts of the detector overlapped. Value from Vincent’s study. Independent MC sample
sysP | 0 ~0.8 | The purity systematic is extracted independently for LL and LO. No correlation? Highly correlated but not sure how much.
Correlations between two triggers (same kin bin) : ρstat = 0, ρsysA = 0 , ρsysP = 0.8

## Slide 7: Step3 : Combine period, and sysW
P01
P02
…
P08
xsc3D
+/- stat
+/- sysA
+/- sysP
+/- sysT
+/- sysW
Step3 :
Combine
period
Different data sample, use BLUE to combine
Weights | BLUE
Combine mean | BLUE and only stat error as weighting, check both mind empty bins from each period; luminasity
Combine error | BLUE
sysW | Half size of (max-min) ; 0
stat | 0 | Different periods are different data: no shared events.
sysA | 0 | Each period has its own MC production: acceptance systematic extracted independently.
sysP | 1 | One common estimate for all periods. It does not average down and sets an error floor.
sysT | 1 | 
Correlation between periods (same kin bin) : ρstat = ρsysA =0, ρsysT = 1 · ρsysP = 1
xsc3D +/- stat +/- sysA +/- sysP +/- sysT
xsc3D +/- stat +/- sysA +/- sysP +/- sysT
xsc3D +/- stat +/- sysA +/- sysP +/- sysT
Notes: Any weights with Σ wi = 1 give an unbiased mean. A wrong ρ only costs precision; it does not shift the central value.

## Slide 9: Check w/ step4 to make sure rho_kinematics before doing step#3?
P01
P02
…
P08
xsc3D
+/- stat
+/- sysA
+/- sysP
+/- sysT
+/- sysW
Step3 :
Combine
period
P01 0D
Step4 : Integration
Make sure rho
P01 3D
P02 0D
P02 3D
P08 0D
P01 3D
…
…

## Slide 10: Step 4 : Integration
xsc3D
+/- stat
+/- sysA
+/- sysP
+/- sysT
+/- sysW
xsc2D
xsc1D
+/- stat
+/- sysA
+/- sysP
+/- sysT
+/- sysW+/-
Step4 : Integration
Introduce correlation between kinematics for each systematic terms.
Integrated value | XK = Σj∈K Xj 3D bins j summed into bin K of xsc2D or xsc1D (× bin width if differential)
Uncertainty, per source k | σk,K2 = Σj σk,j2 + ρk Σj≠l σk,j σk,l
Two limits | ρ = 0: quadrature (smallest). ρ = 1: linear sum (largest, the safe choice if unsure).
Correlation between kinematics
stat | 0 |  | Different bins hold different events (if events migrate between bins, add off-diagonal terms).
sysA | ≈ 0.8 |  | One MC production per period: modelling part is coherent, MC-stat part is independent. Borrowed from LL/LO, to test in 0.5–1.
sysP | ≈ 1 |  | One global procedure (not per period), so a method offset should be coherent. Sign test on the next slide.
sysT | ? |  | Placeholder 0.5: fluctuation part is independent, coherent part (e.g. trigger turn-on) is shared. Pull test on the next slide.
sysW | ? (0) |  | Not added for now (sysW = 0).

## Slide 11: Summary : ρ used at each step
Source | Step 1 Purity (pV vs pC) | Step 2 Trigger (LL vs LO) | Step 3 Period (P01 … P08) | Step 4 Integration (between bins)
stat | 1 | 0 | 0 | 0
sysA | 1 | 0 | 0 | ≈ 0.8
sysP | new | 0.8 | 1 | ≈ 1
sysT | – | new | 0 | ? (0.5)
sysW | – | – | new (0) | ? (0)
ρ = 0: errors add in quadrature.
ρ = 1: errors add linearly .
new: systematic created at this step (half of the difference).

## Slide 12: Other
2D xsc (not integrated from 3D)
1D xsc (not integrated from 3D)
In the end 0D error has to be consistent no matter 2D/1D xsc are integrated, we might use it to guess correlations need to be used. I will think about it.

## Slide 13: Code Framework for DY Systematics
run_all.sh (Linux / Git Bash / WSL) run_all.bat (Windows)
runs step 1 → 2 → 3 → 4 for every target / trigger / week, each step reads the folder written by the previous one, stops at the first error
options of every script: --input-dir --output-dir --target --trigger --week --logy --fmt
INPUT raw 3D cross sections
96 purity results
2 purity × 3 targets × 2 triggers × 8 weeks
= 96 results, in 48 files (V and C side by side)
columns (12)
6 bin edges + xscV staV sysA_V + xscC staC sysA_C
STEP 1 combine purity
step1_combine_purity.py
done · 96 → 48 files
xsc = (xscV + xscC)/2
sysP = |xscV − xscC|/2
ρ_stat = ρ_sysA = 1
check plots
xsc vs xF per (m, pT) bin:
xscV, xscC before; combined after;
stat, sysA, sysP each its own bar; + σ/xsc per source
STEP 2 combine trigger
step2_combine_trigger.py
next · 48 → 24 files
BLUE of LL and LO, bin by bin
sysT = |x_LL − x_LO|/2
ρ_sysA ≈ 0.8, ρ_stat = ρ_sysP = 0
check plots
xsc_LL, xsc_LO before; combined after;
stat, sysA, sysP, sysT each separate; + σ/xsc per source
STEP 3 combine period
step3_combine_period.py
planned · 24 → 3 files
weighted mean of P01 … P08
sysP fully correlated (ρ = 1)
sysW = 0, χ²/ndf check
check plots
P01 … P08 before; combined after;
every source separate
STEP 4 integration
step4_integrate.py
planned · 3 → 3 (1D) + 9 (2D)
X_K = Σ_j X_j, ρ between 3D bins
ρ_sysA ≈ 0.8, ρ_sysP ≈ 1, ρ_sysT = ? (0.5)
ρ_stat = 0, sysW = 0
check plots
3D vs 1D (m, pT, xF)
2D (m-pT, m-xF, xF-pT)
dysys_common.py shared by every step
settings · column layouts · reading / writing tables · helpers: BLUE weights, weighted mean, ρ sum, plot style

## Slide 14: Step by Step: Recipe, Outputs and Check Plots
 | Step 1 combine purity | Step 2 combine trigger | Step 3 combine period | Step 4 integration
Script | step1_combine_purity.py | step2_combine_trigger.py | step3_combine_period.py | step4_integrate.py
Reads (--input-dir) | raw xsc3D: 48 files, each with V and C columns (96 purity results) | step 1 results, LL and LO of the same target and week | step 2 results, P01 … P08 of one target (24 files) | step 3 results, one 3D file per target (3 files)
Recipe | xsc = (xscV + xscC)/2; stat, sysA averaged; sysP = ¦xscV − xscC¦/2 | BLUE per bin, cov = ρ_sysA σ_LL σ_LO; each source with the same weights; sysT = ¦x_LL − x_LO¦/2 | w ∝ 1/σ²_u, σ²_u = stat² + sysA² + sysT²; sysP kept common | X_K = Σ_j X_j; σ²_k,K = Σσ²_k,j + ρ_k Σ_j≠l σ_k,j σ_k,l
Correlations | ρ_stat = ρ_sysA = 1 | ρ_stat = 0, ρ_sysA ≈ 0.8, ρ_sysP = 0 | ρ_stat = ρ_sysA = ρ_sysT = 0, ρ_sysP = 1, sysW = 0 | ρ_stat = 0, ρ_sysA ≈ 0.8, ρ_sysP ≈ 1, ρ_sysT = ? (0.5), sysW = 0
Writes (--output-dir) | xsc stat sysA sysP 48 files in step1_out/ | xsc stat sysA sysP sysT 24 files in step2_out/ | xsc stat sysA sysP sysT 3 files in step3_out/ | 1D: 3 files (one per target) 2D: 9 files (3 targets × m-pT, m-xF, xF-pT) in step4_out/
Check plots | xsc vs xF in each (m, pT) bin: xscV, xscC before; combined after, each error source its own bar (stat, sysA, sysP); 2nd plot: σ/xsc [%] per source | same layout: xsc_LL, xsc_LO before; combined after; stat, sysA, sysP, sysT each separate; 2nd plot: σ/xsc per source | same layout: P01 … P08 before; combined after; every source separate; 2nd plot: σ/xsc per source; χ²/ndf vs xF | 3D vs 1D (m, pT, xF) and 2D (m-pT, m-xF, xF-pT) at ρ = 0, nominal, 1; every source separate; Σ 3D = integrated
Every script also takes --target --trigger --week --logy --fmt and prints diagnostics for the assumptions it uses.